//  Building Lights ON OFF Random Cycling with Control Pin

//  Modified by K. Hackleman Nov 2017

//

int tim_delay = 2000;

int control_pin = 14;   //Control Pin is Pin 14 (A0) Low/Ground is OFF

// OPEN (Unattachd) Pin is ON

#define numleds  18     //Number of LED's plus 1

byte ledpins[]={1,2,3,4,5,6,7,8,9,10,11,12,13,15,16,17,18,19};

//LEDs (Anode/Plus side) attach to these pins, except pin 1

void setup() {

pinMode(control_pin,INPUT_PULLUP);

// initialize the digital pins as an outputs and set OFF

for (int i=1; i< numleds; i++) {

pinMode(ledpins[i], OUTPUT);

digitalWrite(ledpins[i], LOW);

}

for (int i=0; i< numleds; i++) {   //As a test turn all ON in sequence

digitalWrite(ledpins[i], HIGH);

delay (tim_delay/30);

}

delay( tim_delay/3);

for (int i=0; i< numleds; i++) {  //Now turn all OFF in sequence

digitalWrite(ledpins[i], LOW);

delay (tim_delay/30);

}

}

void loop() {

digitalWrite(ledpins [random (0,numleds+1)], lightsw() );

delay(tim_delay);              // wait for a bit

}

boolean lightsw() {

if (digitalRead(control_pin) == LOW) return LOW;  //Eventually turn all lights OFF

if (random(0,100)>40) return HIGH;  //40 represents a 60% ON time

else return LOW;

}